## Slide 1: Restaurant Design
Group 2
Caio Beojone
Murat Genc
Marti Montesinos
Jangwon Park

## Slide 2
Scenario Description
A restaurant
  has space for up to 400 seats
  various table sizes (for 2, 3, 4 and 5 customers)
    different table arrangements constrained by the number of seats
  table arrangements to be made at the beginning of the opening time
    not possible to split a group into different tables
    not possible to merge the tables
    groups can sit together

## Slide 3
Scenario Description (cont.)
Customer Arrival (arrival rate: c)
  Groups start arriving at 19:00 till 22:00
    No arrival after 22:00 –> available service for customers in the queue
  are non-homogenous and vary among group sizes (group size: g)

## Slide 4
Scenario Description (cont.)
Service and Customer Behavior
  Customer Abandonment: customers in the queue may decide to wait or leave (every five minutes)
  duration of a dinner (d)
    40 + t ~ exp (0.05) minutes
  immediate table availability for the next customer
  assumption: adequate staff capability and capacity

## Slide 5
Scenario Description (cont.)
Billing
  Bill per person: b
    Proportional to the dinner duration (d) –> b = d * r
  Customer-specific consumption rate (r)
    r ~ unif (0.5, 1.2) –> € / minute
  Sharing a table
    decreased dinner duration –> d’ = d * 0.5
    decreased consumption rate –> r’ = r * 0.8
Profit = b * ( # of customers served ) – ( € 0.10 * total operating time)

## Slide 6: Problem Description
Running a successful business by
  Maximizing the total profit of a restaurant
Decision variables:
  Table arrangement (table size and quantity)
  Seating policy for arriving customers
Evaluation of success
  Defined parameters (described in the Simulation part)

## Slide 7: Simulation

## Slide 8: Discrete Event Simulation
Running a simulation of a scenario
  Input parameters described in the previous section
  Different scenarios for varying table arrangement and seating policy
State(s)
  Time / # of customers in the system
Indicators
  Profit
  # of admissions
  # of abandonments
  Max queue length
  …

## Slide 9: Discrete Event Simulation (cont.)
Events
  Events that occur at time “t”
    Arrival
      always the first event
    Dinner Duration
      refers to being served
    Abandonment
      A customer leaves the system
    Simulation End

## Slide 10
Table Arrangement
Default arrangements
  # of tables [size 1, size 2, size 3, size 4, size 5]
    Arrangement 1: [0, 0, 0, 0, 40]
    Arrangement 2: [0, 50, 0, 0, 20]
Modified arrangements
    Arrangement 3: [0, 37, 15, 10, 8]
      Arranged according to the arrival rate

## Slide 11
Table Arrangement (cont.)
Default arrangements
  # of tables [size 1, size 2, size 3, size 4, size 5]
    Arrangement 1: [0, 0, 0, 0, 40]
    Arrangement 2: [0, 50, 0, 0, 20]
Modified arrangements
    Arrangement 3: [0, 37, 15, 10, 8]
      Arranged according to the arrival rate

## Slide 12
Seating Policy
Initial approach:
  First-come, First-served basis

## Slide 13
Seating Policy (cont.)
Modified approach:
  Reservation Policy
  Consisting the reservation of a table (size n) to a group (size n)
  First-come, first-served policy except the “prioritized customers”

## Slide 14
Method:
  Control Variate;
  Number of groups that arrived;
Usual number of runs: 100 (minimum accepted);
Variance Reduction

## Slide 15
Table arrangement:
  200 seats;
  40 tables size 5;
Simulation results

## Slide 16
Simulation

## Slide 17
Simulation

## Slide 18: Optimization

## Slide 19
Decision variables
  Number of tables of each type:
  Seating policy for arriving customers is fixed
Single-objective function:
  Customer revenues – Operation costs
  Other indicators may impact the long-term profit
    e.g. abandonments  customer satisfaction  Future demand
    Approach: sensitivity analysis (& ε-constrained opt)
Problem Description
Notes: According to the problem definition we have only one objective: maximize the profit
The mean profit we get for a day is the best proxy of the total profits in a week or a month. We have already seen that the distribution of the profit is unimodal, so the mean is a good indicator.
In the long-run the number of abandonments could impact the business. The unserved customers are clearly unsatisfied and they may not want to visit again the restaurant in the future. Therefore, we also analyze the impact of the different table arrangements and seating policies in the number of abandonments. A high number of abandonments will impact negatively our future demand.
As there’s no clear way to compare profit & abandonments, epsilon constrained optimization could be a good option. But first, we need to analyze the trade-offs between profit and abandonments. Then we can impose an upper bound for the abandonments.

## Slide 20
  Merge/Split tables
    Number of seats remains constant
    Neighborhood size
  Add/Remove tables
    Number of seats changes
    Neighborhood size
Neighborhoods
4
2
2
4
2
2
4
2
2
2
2
2
2
4
2
2
4
2
2
4
2
2
2
2
Notes: Mention the order we use them
-To refine a solution (find a local optimum)
-To escape from a local optimum

## Slide 21
  Merge/Split tables
    Number of seats remains constant
    Neighborhood size
  Add/Remove tables
    Number of seats changes
    Neighborhood size
Neighborhoods
4
2
2
4
2
2
4
2
2
2
2
2
2
4
2
2
4
2
2
4
2
2
2
2
Refine a solution
Escape from a
local optimum
Notes: Mention the order we use them
-To refine a solution (find a local optimum)
-To escape from a local optimum

## Slide 22
Neighborhood structures:
  Merge/Split & Add/Remove
  When the neighborhood gets to large  limited search (max k neighbors)
If the starting point is off, very long search
  Bad starting point
    =300, greedy table arrangement
    Merge/Split moves 
    Add/Remove 
  Alternatives
    = rest. service rate 
Baseline VNS
Caio’s new graph:
Replicate this class figure with n=300, group the neighborhoods in Merge, Split, Add, Remove or just show the seats evolution (we see if Merge/Split or Add/Remove)
Notes: It is not obvious which is the best starting point. For instance if the demand varies a lot along the opening hours.
Explain that starting point of 200 seats perfomed better than 210

## Slide 23
Neighborhood structures:
  Merge/Split & Add/Remove
  When the neighborhood gets to large  limited search (max k neighbors)
If the starting point is off, very long search
  Bad starting point
    =300, greedy table arrangement
    Merge/Split moves 
    Add/Remove 
  Alternatives
    = rest. service rate 
Baseline VNS
Caio’s new graph:
Replicate this class figure with n=200 or 210, group the neighborhoods in Merge, Split, Add, Remove or just show the seats evolution (we see if Merge/Split or Add/Remove)
Notes: It is not obvious which is the best starting point. For instance if the demand varies a lot along the opening hours.
Explain that starting point of 200 seats perfomed better than 210

## Slide 24
Limitation of baseline VNS
Size of the neighborhood grows non-linearly. Example: “adding tables”
Reducing the Neighborhood Size
4+n-1Cn
where n = number of tables to add
Increasingly more costly to check a sufficiently large number of neighbors.
Limiting the neighborhood size will likely lead to suboptimal profit.

## Slide 25: Golden Section Method
Idea
The new restaurant can have anywhere from 200 to 400 seats.
Successively narrow this interval by optimizing mean profit at discrete points.
In the beginning, use a greedy heuristic to quickly narrow down the interval.
When the interval becomes “small enough”, use VNS.
We can eliminate the neighborhood structure for adding/removing tables.

## Slide 26: Golden Section Method
Conditions
Mean profit as a function of number of seats must be concave (unimodal).
In the interval that greedy heuristic eliminates, its results must be consistent with the results of VNS.
e.g. fgreedy(300) > fgreedy(350)  fVNS(300) > fVNS(350)

## Slide 27: Golden Section Method

## Slide 28: Golden Section Method

## Slide 29: Golden Section Method

## Slide 30: Golden Section Method
Our parameters
Threshold for switching: 50
Tolerance for termination: 5
Threshold:
Greedy => VNS
Final interval

## Slide 31
Baseline VNS
Results: Baseline VNS vs. Golden Section VNS

## Slide 32
Golden section VNS
Results: Baseline VNS vs. Golden Section VNS
Iteration | Left Extreme | Right Extreme
1 | 200 | 323.6
2 | 200 | 276.4
3 | 200 | 247.2152
4 | 200 | 229.1848
5 | 200 | 218.0362
6 | 200 | 211.1486
7 | 200 | 206.8898
8 | 200 | 204.2588
STOP
Switch

## Slide 33
Results: Baseline VNS vs. Golden Section VNS

## Slide 34
Results: Baseline VNS vs. Golden Section VNS
Method | Mean Profit | Optimal Table Arrangement | Optimal Number of Seats
Baseline | $13,662 | Size 2: 14 tables Size 3: 17 tables Size 4: 13 tables Size 5: 12 tables | 191
Golden Section | $13,781 | Size 2: 21 tables Size 3: 15 tables Size 4: 13 tables Size 5: 13 tables | 204

## Slide 35
Results: Seating Policy Comparison

## Slide 36
Results: Seating Policy Comparison
Policy | Mean Profit | Optimal Table Arrangement | Optimal Number of Seats
Default | $13,781 | Size 2: 21 tables Size 3: 15 tables Size 4: 13 tables Size 5: 13 tables | 204
Reservation | $13,865 | Size 2: 19 tables Size 3: 15 tables Size 4: 11 tables Size 5: 15 tables | 202
Notes: Reduced tables of size 2 and 4 by two and gave them all to size 5 tables.
Otherwise, the number of seats remain more or less the same.

## Slide 37
Results: Seating Policy Comparison
Seating Policy 1
Seating Policy 2
Notes: Reduced proportion of customer groups of size 5 who abandoned by roughly 13% at a relatively small cost of losing 1.5% more of customer groups of size 3. The rest remains more or less the same.

## Slide 38
Results: Summary
Our solution as a way to:
Prevent customers from leaving the restaurant
But not increase the average number of occasions of sharing tables significantly
Golden section VNS (policy 2)
Mean Profit: 13,865
Golden section VNS (policy 1)
Mean Profit: 13,781
Naïve Solution
Mean Profit: 11,419
Greedy Solution
Mean Profit: 12,238

## Slide 39
Results: Summary
Our solution as a way to:
Prevent customers from leaving our restaurant
But not increase the average number of occasions of sharing tables significantly
  Avg. number of customers who share tables (per day):
Naïve solution: 6.5
Greedy solution: 1.1
Golden section VNS (policy 1): 1.1
Golden section VNS (policy 2): 1.3